## Slide 1: Lockout and Tagout Sedgwick Risk Services Presented by Sedgwick on behalf of ORM March 2020

## Slide 2: Disclaimer
The information contained herein is not intended as legal advice, is advisory only; provided on an “as is” basis, and to be used solely at the user’s risk. The information is made available without any warranty of any kind and, to the extent allowed by law, Sedgwick disclaims any and all implied warranties and representations. All procedures and training, whether required by law or not, should be implemented and reviewed by safety and risk management professionals and legal counsel to ensure that all local, state, and federal requirements are satisfied. Sedgwick disclaims any and all liability that may arise in connection with a user’s use of this information.

## Slide 3: Course Outline – Lockout and Tagout
  Why Take Lockout and Tagout Training?
  Definitions
  Types of Hazardous Energy
  Energy Control Procedure
  Start-up Procedures
  Additional Lockout/Tagout Requirements
  Summary

## Slide 4: Why Take Lockout and Tagout Training?
It is important for everyone’s safety!
The Lockout/Tagout practices:
    Requires Agencies to establish a program and utilize procedures for affixing appropriate lockout or tagout devices to energy isolating devices.
    To otherwise disable machines or equipment to prevent unexpected energization, start up or release of stored energy in order to prevent injury to employees.

## Slide 5: Definitions
Affected employee:
    An employee whose job requires him or her to operate or use a machine or equipment, which needs servicing or maintenance.
Authorized employee:
    A person who locks out or tags out machines or equipment in order to perform servicing or maintenance on that machine or equipment.
Hardware:
    A device that is attached to the energy isolating device to physically prevent it from being moved from the OFF position.

## Slide 6: Definitions
  Energy isolating device:
    A mechanical device that physically prevents the transmission or release of energy when in the OFF position such as a gate valve or a circuit breaker.
    DOES NOT include:
      On/off switches
      Push buttons
      Control circuit devices
  Zero energy state:
    All stored or residual energy has been released, restrained or dissipated.
    Equipment can’t be energized or turned on.

## Slide 7: Types of Hazardous Energy
There are several types of hazardous energy which can injure an employee.
  These include but are not limited to:
    Electrical
    Mechanical
    Chemical
    Thermal
    Hydraulic
    Pneumatic

## Slide 8: Types of Hazardous Energy
Electrical energy:
  Most common energy type.
  Electrical storage devices such as batteries & capacitors.
  Panelboards house circuit breakers for distribution of electricity.
    Panelboards are also energy isolating devices and provide overcurrent protection.

## Slide 9: Types of Hazardous Energy
    Electrical energy (continued):
  Disconnects are common electrical energy isolating devices.
  Injuries:
    Electrocution
    Electric shock
    Burns

## Slide 10: Types of Hazardous Energy
    Mechanical energy:
  Energy is manifested through motion and energy is associated with moving parts of a mechanical system:
    Power transmission apparatus
    Fly wheels
    Belts
    Pulleys
  Contact with moving parts can crush, fracture, cut, or amputate a body part.

## Slide 11: Types of Hazardous Energy
    Potential energy:
  Potential energy is stored energy that can be hazardous if released. Some examples of potential energy include:
    Gravity
    Springs
    Thermal energy
    Stored energy
    Capacitors

## Slide 12: Types of Hazardous Energy
    Pneumatic energy:
  Pneumatic lines and vessels can retain energy in the form of stored pressure which may have to be relieved prior to servicing or maintenance.
  This may be encountered in:
    Pressurized systems
    Compressors
    House air
    Air powered tools
    Other gases

## Slide 13: Energy Control Procedure
    Energy control procedure:
  A written procedure, developed to protect employees who perform maintenance on machines, equipment and processes where hazardous energy sources are present.
  A hazardous energy control procedure shall be developed and utilized by the Agency when employees are engaged in the cleaning, repairing, servicing, setting-up or adjusting of:
    Prime movers
    Machinery
    Equipment

## Slide 14: Energy Control Procedure
    Process of energy control procedure implementation:
  There are six steps:
    Prepare for shutdown
    Shutdown
    Isolate energy sources
    Apply locks & tags
    Control residual energy
    Verify energy control methods

## Slide 15: Energy Control Procedure
    Step 1 - Prepare for shutdown:
  Notify affected employees of activities.
  Use energy control procedure data to prepare for shutdown:
    Identify shutdown procedures.
    Identify energy sources.
    Identify energy isolation devices.
    Determine quantity and type of lockout and tagout devices required.

## Slide 16: Energy Control Procedure
    Step 2 - Shutdown:
  Shut equipment down by its normal stop/start method.
    This can include an on/off switch, a toggle switch, or typical machine start/stop method.

## Slide 17: Energy Control Procedure
    Step 3 - Isolate energy sources:
  Isolate all energy sources from the machinery or equipment.
    This may include using energy isolating devices, i.e., circuit breakers, valves, etc.

## Slide 18: Energy Control Procedure
    Step 4 – Apply locks and tags:
  Apply locks, tags and hardware to energy isolating devices in OFF position.
  Signs, tags, padlocks, and seals shall have means by which they can be readily secured to the controls.
    Group lockout:
  One lock/tag per individual per energy isolating device!
  Each person who enters a danger zone must apply his or her own lock/tag!

## Slide 19: Energy Control Procedure
    Step 4 – Apply locks and tags: (continued):
    Group lockout (continued):
  Must provide the same level of protection as individual lockout/tagout through the use of hasps, group lockout boxes, or other equivalent devices.
  Locks will be placed inside a lock box or hasp, an additional lock will be placed on the outside of lock box or hasp.

## Slide 20: Energy Control Procedure
    Step 5 – Control residual energy:
  This is accomplished by releasing, restraining, or dissipating all residual energy, i.e., bleeding, blocking, or discharging all sources of energy.

## Slide 21: Energy Control Procedure
    Step 6 – Verify energy control methods:
    Verify that energy control measures are effective:
  Ensure that switches, valves and other mechanisms can not be turned on.
  Use a meter to ensure that electrical energy is not present.
  Activate equipment control switches and levers, and depressing start buttons to ensure power is isolated. Then return switches, levers and buttons to the off position.

## Slide 22: Start-up Procedures
    Once repairs/maintenance have been completed:
  Verify all controls are in the neutral or “OFF” position.
  Remove lockout/tagout devices.
  Notify affected employees that lockout/tagout devices have been removed and the equipment or machinery is ready for use

## Slide 23: Additional Lockout/Tagout Requirements
    Auditing:
  The audit of the Lockout/Tagout Program must be performed by an authorized employee [other than the ones(s) utilizing the energy control procedure].
  The audit must be conducted annually.
  A review is also to be performed if a weakness or issue is noted associated with the Lockout/Tagout Program .

## Slide 24: Additional Lockout/Tagout Requirements
    Training requirements:
    Affected employees need to be informed of the procedures and prohibitions relating to attempts to:
  Perform work on equipment
  Restart or re-energize machines or equipment which are locked out or tagged out.
  Who is authorized to perform work on equipment.

## Slide 25: Additional Lockout/Tagout Requirements
    Important instructions for authorized employees:
  Recognition of applicable hazardous energy sources, the type and magnitude of the energy available in the workplace.
  The methods and means necessary for energy isolation and control.
  The purpose and use of the energy control procedure.
  Initial training on the energy control program, the steps and requirements.
  Periodic training as necessary.

## Slide 26: Additional Lockout/Tagout Requirements
    Re-training must be done when:
  There has been a change in an employee’s job assignments.
  There has been a change in machines, equipment or processes that present a new hazard.
  There has been a change in the energy control procedures.
  A periodic inspection reveals, or the Agency has reason to believe, that there are deviations from or inadequacies in the employee's knowledge or use of the energy control procedures.

## Slide 27: Additional Lockout/Tagout Requirements
    Contractors:
  Review work to be done and assure they have and follow controls at least as effective as your Agency’s procedures, and in compliance with all codes.
  Cross-communicate re the Lockout processes with all affected people.
  Audit contractors prior to allowing and periodically to assure adherence to needed controls.

## Slide 28: Summary
    There are several types of hazardous energy which can injure an employee. Lockout and tagout procedures are important to keep everyone safe!
  Ensure your Agency is following the correct guidelines for lockout/tagout, including:
    Start up and group lockout procedures
    Auditing
    Training and retraining

## Slide 29: Summary
    Follow the six steps for energy control procedure:
    Prepare for shutdown
    Shutdown
    Isolate energy sources
    Apply locks & tags
    Control residual energy
    Verify energy control methods

## Slide 30
Thank you | questions