## Slide 1: Heat Stress - Sedgwick Risk Services
Heat Stress - Sedgwick Risk Services

## Slide 2
Disclaimer
The information contained herein is not intended as legal advice, is advisory only; provided on an “as is” basis, and to be used solely at the user’s risk. The information is made available without any warranty of any kind, and, to the extent allowed by law, Sedgwick disclaims any and all implied warranties and representations. All procedures and training, whether required by law or not, should be implemented and reviewed by safety and risk management professionals and legal counsel to ensure that all local, state, and federal requirements are satisfied. Sedgwick disclaims any and all liability that may arise in connection with a user’s use of this information.

## Slide 3: Factors leading to heat stress
High temperature and humidity
Direct sun or heat
Limited air movement
Physical exertion
Poor physical condition
Some medications
Inadequate tolerance for hot workplaces or areas

## Slide 4: Facts about heat stress
A body at work generates heat faster than at rest, often more heat than is needed.
Roughly three-fourths of the stored energy the body draws on during activity converts to heat rather than motion.
More strenuous activity naturally generates more heat.
The elevation of core body temperature disturbs functioning, so the body protects itself by dissipating excess heat.
The mechanisms of widening of blood vessels and sweating are critical to moving heat from a human body to the environment.

## Slide 5: How the Body Copes with Heat
Working where it is hot puts stress on your body’s cooling system.
Your body is always generating heat and passing it to the environment via sweat or simple body surface cooling.
The harder your body is working the more heat it has to lose.
When the environment is hot or humid or has the sun as a source of radiant heat, your body must work harder to rid of its heat.

## Slide 6: Know the Symptoms
Heat cramps:
Symptoms: Painful spasms of leg, arm or abdominal muscles, heavy sweating, and thirst.
Causes: Typically occur during or after hard work or exercise and are caused by electrolyte deficiencies that result from extended periods of intense sweating.

## Slide 7: Know the Symptoms
Heat Exhaustion Symptoms:
Heavy sweating
Headache
Clumsiness, dizziness
Exhaustion, weakness
Irritability
Fainting/Light-headedness
Paleness
Nausea or vomiting

## Slide 8: Know the Symptoms
Heat Stroke Symptoms:
Sweating may or may not be present
Red or flushed, hot, dry skin
Confusion/Bizarre behavior
Collapse
Panting/Rapid breathing
Altered levels of consciousness
Rapid, weak pulse
Convulsions before or during cooling

## Slide 9: Know How to Respond
If Heat Stroke, call 911 immediately and transport as soon as possible. Heat stroke can be life threatening.
Seconds count—cool the person rapidly using whatever methods you can. Consider a cool shower, spray cool water from a garden hose, apply a damp cloth. Continue monitoring the person until medical help arrives—stay with them.

## Slide 10: Know How to Respond
For either Heat Exhaustion or Heat Stroke:
Move the person to a cool, shaded area to rest; do not leave them alone.
Loosen and remove heavy clothing that restricts evaporative cooling.
Give cool water to drink, about a cup every 15min.

## Slide 11: Know How to Respond
For either Heat Exhaustion or Heat Stroke:
Drinking water is to be in plenty of convenient, visible locations close to the work area
Fan the person, spray cool water, or apply a damp cloth to their skin to increase evaporative cooling
When responding remember to—Keep calm and cool!

## Slide 12: Questions? Thank you

## Slide 13
Click to edit Master text styles
  Second level
    Third level
      Fourth level
        Fifth level